## Slide 1: SCATTERER RECONSTRUCTION AND PARAMETRIZATION OF HOMOGENEOUS TISSUE FOR ULTRASOUND IMAGE SIMULATION
Our method (inverse problem)
  Open problem: How to find distribution of scatterer values which creates a given image of ultrasound tissue?
  Scatterer representation allows simulation of tissue with arbitrary US parameters
  Problem can be expressed as linear system with convolution matrix A, solving for scatterer image x
  Scatterers typically assumed to be sparse and pointlike → we formulate system as L1 total variational regularization
  Solve system using convex optimization
Simulation pipeline
  Reconstruct scatterer image for homogenous patch of tissue
  Estimate scatterer density and distribution N(µ,σ) of amplitude values from reconstructed scatterers
  Instantiate new scatterers to fill arbitrary volume
  Plug instantiated scatterers into forward simulation pipeline
Oliver Mattausch and Orcun Goksel
x
b
arg min.
speckle image
scatterer image
s.t. x≥0
Ultrasound simulation (forward problem)
  Important for training of sonographers
  Characteristic ultrasound tissue (i.e., speckles) due to scattering with microscopic (unobservable) reflectors
  Scatterers often modelled using parametrization [Bürger13]
  Realistic and efficient speckle simulation due to convolution of parametrized scatterer image with US point-spread function
convolution matrix
scatterer image
speckle image
Tissue reconstruction and simulation results
PSF
Computer phantom
Pelvic phantom (using 3 tissue samples)
Original
Synthesized
[Bürger13] B. Bürger, S. Bettinghausen, Radle M., and J. Hesser. Real-time gpu-based ultrasound simulation using deformable mesh models. IEEE Trans. Med. Imaging, 32(3):609–618, 2013.
estimated parametrization
*
=
scatterer image resolution 1282
scatterer image resolution 2156x256

## Slide 2
Ultrasound speckles
Future work
  Use in actual 3D ultrasound simulation (currently only 2D)
  Quantitative evaluation of simulated results