## Slide 1: Monte-Carlo Ray-Tracing for Realistic Interactive Ultrasound Simulation
Oliver Mattausch, Orcun Goksel
Computer-assisted Applications in Medicine (CAiM)

## Slide 2: Ultrasound (US) Simulation for Training
Ultrasound: radiation-free, low-cost, real-time
Low SNR + ultrasound artifacts require training
Training difficult, e.g., of rare pathologies
Few volunteers for transvaginal, transrectal, biopsy
Huge potential for interactive VR simulator
Goal: plausible simulation for experts
US image of pregnancy
Notes: Remove lines in template Motivation: Transvaginal, transrectal ultrasound, biopsy (no volunteers)

## Slide 3: Ultrasound Image Generation
transducer elements (128-256 crystals)
beam forming due to negative/positive interference
many element transmitting
single element receiving echo, creating radio-frequency (RF) line
beamformed point-spread function

## Slide 4: Ultrasound Image Generation
Ultrasound speckle interactions with microscopic structures (<wavelength) act like point scatterers
Reflections interactions with large-scale structures (≫wavelength) dictated by Snell’s law
Ultrasound artifacts e.g., shadows due to beam refractions
US image of pregnancy
Notes: 3 things are important for a realistic ultrasound image.
Specify terms: speckles, reflections, ultrasound artifacts Explain accustic impedance differences as us propagates, if objects larger than wavelength, they act like point scatterers

## Slide 5: Raytracing-Based Ultrasound Simulation
Handles large-scale interactions
Input:
  CT image [Salehi et al. MICCAI15]
  Triangle model [Bürger et al. TMI13] (most flexible)
human anatomy model
artificial phantom

## Slide 6: Raytracing-Based Ultrasound Simulation
Binary deterministic raytracing [Whitted80]
Problems: exponential complexity poor parallelism on GPU
reflection
refraction
shoot ray/RF line
Snell’s law (ratio of impedances)
tissue 1
tissue 2
tissue 3
Notes: These methods use deterministic ray tracing, also known as Whitted Raytracing in the CG community.

## Slide 7: Convolution-Based Ultrasound Simulation
Handles small-scale interactions
Linear approximation of full wave interactions [Karamalis10, Jensen04]
Fast separable convolution on GPU: COLE [Gao et al. TUFFC09]
convolution
tissue representation (scatterer map)
ultrasound speckle
*
=

## Slide 8: Convolution-based Ultrasound Simulation: Tissue Model
values can be automatically derived from images [Mattausch and Goksel EMBC15]
(μ, σ)
after convolution with PSF
3-parameter tissue model (μ, σ, ρ)
(ρ)
tissue representation
Notes: Left side afterwards, in references conference name first
Rho: probability of non-zero pixel value

## Slide 9: State of the Art: Issues
Deterministic model: Infinitely thin perfectly specular surfaces
3-parameter tissue model: uniform (toy-like) speckle
in-vivo pregnancy
deterministic raytracing + convolution
Notes: Comparing the state-of-the art simulation with an actual pregnancy, several issues become apparent.
Add snells law
Orthogonal reflections show up

## Slide 10: Our Contributions
Improved surface model
Efficient evaluation using Monte-Carlo raytracing
Improved volumetric tissue model

## Slide 11: Improved Surface Model: Roughness
specular surface model
surface roughness model
Notes: In contrast to the perfectly specular surfaces of previous approaches, we propose that real surfaces have imperfections, causing the surface normal to wiggle wrt. a cosine distribution, where n models the surface roughness.
Snell’s law, not cos infinity before defining model, put profile here of cos distribution

## Slide 12: Improved Surface Model: Roughness
cos∞ distr.
cos100 distr.
cos10 distr.
hypoechoic ‘whiskers’ due to refractions
fluid-filled spherical object
in-vivo example
Notes: To show the possibilities of the surface roughness model, a simulation of a fluid-filled spherical object is used.
Increasing the surface roughness causes the shadow softness to increase. In practice, this parameter has to be adjusted to fit a target appearance. As comparison, this is an-vivo example.
explain how a typical sphere artifact should look like (basically the hyopechoic "whiskers" behind small angle surface due to refraction bending the rays and "shadowing" those area). You can may be show a sample example image with bladder or a cyst, highlighting those shadows. Also, motivate the importance of showing those shadows correctly, by mentioning that the (whisker) shadows are important for the doctor to infer the content of (diagnose) inclusions from their acoustic impedance difference.

## Slide 13: Improved Surface Model: Thickness
flat surface model
surface thickness model
Notes: Hence, in contrast to the infinitely flat surfaces of previous approaches, we propose that real surfaces have finite surface thickness, allowing a ray to penetrate further into a tissue wrt. to a surface thickness parameter.

## Slide 14: Improved Surface Model: (Bone) Thickness
0mm
3mm
6mm
9mm
in-vivo bone image
Notes: In the first image, the bone structure is generated with zero thickness, looking artificial and lacking similarity to an actual bone image.
put the actual US image, perhaps on the left or right of all images (with same areas that you indicate marked/circled) as a ground-truth and visual comparison from the slide start

## Slide 15: Efficient evaluation using Monte-Carlo Raytracing
PT
US signal after surface intersection PT
Intractable for deterministic methods
recursive formulation
integrate over hemisphere
linear complexity easily parallelizable
stochastic ray paths
Notes: Next, I show how to solve our surface model efficiently.

## Slide 16: Monte-Carlo Raytracing
reduce path contribution wrt. d
Snell’s law gives centerline of beam
d
path weighting
transducer elements
beam forming

## Slide 17: Monte-Carlo Raytracing: Initialization
finite transducer thickness
perturbed ray origins
image plane
Notes: In the simplest version, a ray is generated per element, equally sampling the image plane.

## Slide 18: Improved Volumetric Tissue Model
periphery
gestational sac
bone
reflecting tissue
cross-section of model on image plane
stack-based approach to identify tissue T
rasterize ray segment wrt. tissue parameters
Notes: Ultrasound imaging records a slice of the model in the image plane.

## Slide 19: Improved Volumetric Tissue Model
3-parameter model
improved model
Small-scale variations: μ, σ, ρ
Large-scale variations: magnitude Al, frequency fl
Implement with high- and low-res 3D noise texture
more natural
too uniform
in-vivo tissue
Notes: Our improved tissue model has 5 parameters, the 3 known ones describing small scale variations, and 2 new parameters describing the magnitude and frequency of large-scale variations.
motivation and justification of large scale variations making things look more real was not convincing (also considering that the audience may not appreciate what is a more-real US image). I suggest to point out the homogeneous look of the former method, and say "as you might imagine the anatomy does not look such homogenous and almost like a toy-image" and then mention the larger-scale as "approximating larger scale anatomical variations, giving a realistic organ appearance".

## Slide 20: Results
Implementation: C++ using Nvidia Optix and CUDA 7.0
GPU: NVIDIA GTX 780Ti with 3GB
Pregnancy scene | 255K triangles
Image depth | 8.1cm
Transducer frequency | 7Mhz
Transducer FOV | 99 deg
RF lines | 192
RF depth | 2048
Elevation layers | 5
Notes: Next, I will show some more results from the pregnancy scene, which were created using the following environment.

## Slide 21: Results: Comparison
input 255K triangles
deterministic 2.8 FPS
Monte-Carlo (40 paths) 1.4 FPS
in-vivo image
expert judgement realism: 2 of 7
expert judgement realism: 6.5 of 7
Notes: This is a comparison of previous work and our approach to an in-vivo image. Note that the embryo is not in the same place in the in-vivo image, since we used a detailed model from a different source, whereas the rest of the scene was directly segmented from the source.
Since our goal is for our simulation to look plausible for experts, we asked a gynologist for his opinion, rating the realism of the simulation method on a scale from 1 to 7.
don't say "the embryo may not look *real*". It sounds like we could not achieve our goal. Better to say something like "The embryo may not be at the *same place*, since we used a detailed 3D model of the embryo from a different source, created independently from the US image seen."

## Slide 22: Results: Number of Ray Paths
5 paths 303ms 15K rays/s
25 paths 476ms 50K rays/s
15 paths 384ms 37K rays/s
40 paths 714ms
54K rays/s
deterministic raytracing frame time: 357ms
Notes: This side shows the influence of the number of ray paths on performance and image quality.

## Slide 23: Thank you for your attention!
This work was sponsored by the Swiss Commission for Technology and Innovation (CTI).
simulated image
in-vivo image
Notes: At last, I would like to show you some additional slices of the pregnancy scene simulated with our method and compare it to in-vivo images.

## Slide 24: Frame time wrt. max. recursion level
Max. Recursions | Deterministic | MC 15 rays | MC 25 rays | MC 40 rays
7 | 233 ms | 392 ms | 472 ms | 705 ms
10 | 299 ms | 384 ms | 471 ms | 709 ms
12 | 357 ms | 384 ms | 476 ms | 714 ms

## Slide 25: Conclusions
Presented Monte-Carlo method for interactive US simulation
Can be used in training simulators (huge market potential)
Future work: Evaluation of realism in user study

## Slide 26: Monte-Carlo ray tracing
binary deterministic ray-tracing
Monte-Carlo ray-tracing

## Slide 27: Conclusions
Presented Monte-Carlo method for interactive US simulation
Can be used in training simulators (huge market potential)
Future work: Implement deformation models for animation

## Slide 28: Generative Ultrasound Simulation Methods
Wave simulation
(e.g., Westervelt Equation [Karamalis10], FieldII [Jensen04)])
  High-quality simulation
  Not interactive

## Slide 29: Ultrasound Simulation Methods
Wave simulation (e.g., Westervelt Equation [Karamalis10], FieldII [Jensen04)])
  High-quality simulation
  Not interactive
Convolution-based methods
  Linear approximation of wave interactions
  Convolution of scattering tissue with beamformed Ultrasound PSF
  Fast separable convolution on grid possible (COLE [Gao09])
  Cannot describe large-scale interactions (reflections, refractions)
Interpolative methods [Aigner01, Goksel09]
  Precomputed ultrasound
  Realistic, fast
  Restrictive (e.g., for rare cases), limited FOV, transducer parameters fixed

## Slide 30: Monte-Carlo Ray Tracing
Monte-Carlo ray-tracing
binary deterministic model
reflection
refraction
exponential complexity
linear complexity
stochastic perturbations

## Slide 31: Results
Implementation: C++ using Nvidia Optix and CUDA 7.0
GPU: NVIDIA GTX 780Ti with 3GB
Texture Size RF image size Elevation Layers

## Slide 32: Improved Surface Model: Roughness
refractive shadows
in-vivo examples of fluid-filled objects
Notes: explain how a typical sphere artifact should look like (basically the hyopechoic "whiskers" behind small angle surface due to refraction bending the rays and "shadowing" those area). You can may be show a sample example image with bladder or a cyst, highlighting those shadows. Also, motivate the importance of showing those shadows correctly, by mentioning that the (whisker) shadows are important for the doctor to infer the content of (diagnose) inclusions from their acoustic impedance difference.

## Slide 33: Improved Surface Model (Cyst)